## Slide 1: Predictive ABS Through Predictive Wheel Slip Modulation
Name : Gopinath Madheswaran
Student ID : 2024MT12082
Research Area : Automotive Safety, Signal Processing

## Slide 2: Objectives & Scope
Predict wheel lockup using Entropy based Analysis of Wheel speed signal
Generate lock probability using multi-feature weighted fusion
Design smooth brake pressure modulation (By maintaining Slip 10 – 20%)
Simulate predictive ABS vs traditional ABS
Demonstrate feasibility on ECU software
Scope:
Algorithm development
Simulation & Comparison
Documentation

## Slide 3: Slip Ratio Computation
Purpose
  Slip ratio indicates difference between wheel speed and vehicle speed.
Operational Range
  Optimal slip region:
    10% to 20%
    This range corresponds to maximum tyre-road friction.
    Slip monitoring is continuously used to assess wheel behavior stability.

## Slide 5: Overall System Architecture

## Slide 6: Methodology Adopted
Real-time wheel speed signal acquisition
Feature extraction: Approximate Entropy & Kurtosis
Early lockup prediction logic
Predictive control strategy
Comparison with conventional ABS

## Slide 7: Feature Extraction Strategy
Three statistical features are used:
1. Approximate Entropy
  Measures signal irregularity
  Detects instability in wheel rotation behavior
2. Statistical Kurtosis
  Detects sharp variations in signal distribution
  Identifies impulsive behavior before lock
3. Dominant Frequency
  Detects oscillatory signal characteristics
  Helps identify abnormal wheel motion
These features were selected due to computational efficiency and predictive relevance.

## Slide 8: Lockup Probability Estimation
Multi-feature Weighted Model
  Features are combined using weighted contributions:
  Entropy → 35%
  Kurtosis → 25%
  Frequency → 40%
Output:
Lockup Probability Signal
  This signal represents likelihood of impending wheel lock.

## Slide 9: Predictive Warning Generation
Logic
  If:
    Lock Probability > Threshold
  Then:
    Generate Predictive Warning
Key Capability
  Warning generated before traditional ABS activation
  Enables earlier brake pressure modulation.
The predictive method generated multiple early detection events compared to conventional triggers.

## Slide 10: Current progress
Phase | Status
Initial Research | DONE
Algorithm Development (Unit Level) | DONE
Control Logic | In Progress
Dataset Processing | In Progress
Performance Evaluation | Pending
Final Documentation | Pending

## Slide 11: Key Findings
Predictive indicators identified before slip saturation
Braking Efficiency Improved
Reduced stopping distance in simulation
Software architecture compatible with existing ECUs

## Slide 12: Future Work (Out of Scope)
Validation using real vehicle datasets
Hardware-in-loop testing
Integration with production ABS platform
ML-based adaptive thresholds

## Slide 13: Conclusion
Proposed predictive ABS demonstrates earlier wheel lock detection
and smoother braking response in simulations
Project shows strong potential for next-generation safety systems.